## Slide 1: 19CSE342 Wireless and Mobile Communication Mobile IP
J.Govindarajan

## Slide 2: Agenda
Requirements
Entities and Terminologies
IP Packet Delivery
Agent Discovery
  Agent Advertisement
  Agent Solicitation
Registration
Tunneling and Encapsulation
Optimization
- IP-in-IP Encapsulation
- Minimal Encapsulation
- Generic Routing Encapsulation
Reverse Tunneling
IPv6
IP-Micro Mobility Support
    - Cellular IP
    - Hawall
    - Hierarchical Mobile IPv6

## Slide 3: Traditional IP Packet Delivery to Mobile Device (destination)
R1
R3
IP Packet
Dst: 200.8.4.20
R4
R5
Transmission is Successful
Source
IP Address :
150.10.2.5
Destination IP Address :
200.8.4.20
IP Packet
Dst: 200.8.4.20
IP Packet
Dst: 200.8.4.20
Segment
IP header
IP Packet
Dst: 200.8.4.20
200.8.4.20/16
160.5.10.0/16
IP Packet
Dst: 200.8.4.20

## Slide 4: Traditional IP Packet Delivery to Mobile Device (destination): Address has changed : Packet Drop
R1
R3
IP Packet
Dst: 200.8.4.20
R4
R5
Source
IP Address :
150.10.2.5
Destination IP Address :
160.5.10.5
IP Packet
Dst: 200.8.4.20
IP Packet
Dst: 200.8.4.20
Segment
IP header
200.8.4.20/16
160.5.10.0/16
Moved
Destination is not available: Drop the packet

## Slide 5: Requirements : Mobile Device
To enable mobility in the internet
Mobility should remain invisible to the higher layer protocols (Example: TCP)
  High layers (Example :TCP) should continue to work even if the mobile computer has changed its point of attachment
Remain compatible with all lower layers
Enhancing IP for mobility with minimal overhead in message exchange and flooding.

## Slide 6: Mobile IP
MN - Mobile node
CN - Corresponding Node
HA - Home Agent
FA - Foreign Agent
Mobile node
Correspondent Node
Home Agent
Foreign Agent
Care-Of-Address
current location of the MN
COA types:
FA COA
Co-located COA

## Slide 7: Mobile IP : Data delivery to and from mobile node

## Slide 8: Agent discovery
1) Agent Advertisement
Standard ICMP advertisement
ICMP advertisement - Mobility
R bit (registration)
B-Busy to accept the registration
H-Home Agent
F-Foreign Agent
M-Minimal Encapsulation
G-Generic Encapsulation
r-0 (ignored)
T-Reverse Tunnelling is supported by FA
2) Agent solicitation:
type=9
code=0, if the agent also routes traffic from non-mobile nodes,
code=16, if it does not route anything other than mobile traffic
type=9
length=6 + 4*(number of addresses)
mobile node can send out three solicitations, one per second, as soon as it enters a new network.

## Slide 9: Registration
Inform the HA of the current location for correct forwarding of pack
S bit an MN can specify if it wants the HA to retain prior mobility bindings
B bit -MN also wants to receive the broadcast packets of Home Network
D bit-decapsulation by MN if co-located COA
M-Minimal Encapsulation
G-Generic Encapsulation
r and x-0 (ignored)
Registration If the COA is at the FA
Registration If the COA is co-located
Registration request

## Slide 10: Registration Reply ICMP type =3

## Slide 11: Tunneling and encapsulation
Encapsulation

## Slide 12: IP-in-IP encapsulation

## Slide 13
Minimal encapsulation

## Slide 14
Generic Routing encapsulation

## Slide 15
Protocol fields for GRE according to RFC 2784
Protocol fields for GRE according to RFC 1701

## Slide 16
Optimizations
Change of the foreign agent with an optimized mobile IP

## Slide 17: Reverse tunneling
Need for reverse tunneling
  Firewalls
  Multi-cast
  TTL
Reverse tunneling creates triangle problem in reverse direction
Security problems related to reverse tunnelling need to be resolved.

## Slide 18: Micro mobility vs Macro mobility

## Slide 19: Mobile IP/Cellular IP Architecture

## Slide 20: IP Micro-mobility

## Slide 21: IP Micro-mobility : Cellular IP

## Slide 22: HAWAII
Architecture of HAWAII (Handoff-Aware Wireless Access Internet Infrastructure, Protocol)

## Slide 23: Hierarchical Mobile IP (MIPv6 )
Mobility Anchor Point
access routers

## Slide 24: IPv6 and Mobility
Features of IPv6:
  Stateless address autoconfiguration
  Optional NAT (Network Address Translation)
  Easier administration with DHCPv6
  Improved quality of service with flow labeling
IP address Format

## Slide 25: IPv6 address
Aggregatable Global Address
Link-Local Address
IPv4-Compatible IPv6 Address
Unique Local Address

## Slide 26: Aggregatable Global Address
Aggregatable global addresses are used on links that are aggregated upward through organizations, and eventually to the Internet service providers (ISPs).

## Slide 27: Link-Local Address

## Slide 28: IPv4-Compatible IPv6 Address

## Slide 29: Unique Local Address

## Slide 30: IPv6 and Mobile IP
Every mobile node is able to create or obtain a topologically correct address for the current point of attachment.
Every IPv6 node can send binding updates to another node, so the MN can send its current COA directly to the CN and HA.
A soft handover is possible with IPv6.
The FA is not needed any more.
CN only has to be able to process binding updates, i.e., to create or to update an entry in the routing cache
The MN itself has to be able to decapsulate packets, to detect when it needs a new COA, and to determine when to send binding updates to the HA and CN. A HA must be able to encapsulate packets.

## Slide 31
DHCP